## Slide 1: Physical Security Description
To address the threats, vulnerabilities, and countermeasures
  Which can be utilized to physically protect an enterprise’s resources and sensitive information
  Including people, facilities, data, equipment, support systems, media, and supplies
To discuss considerations for choosing
  A secure site, its design and configuration
  The methods for securing the facility against unauthorized access, theft of equipment and information
  The environmental and safety measures needed to protect people, the facility, and its resources

## Slide 2: Physical Security Threats
Natural / environmental
  Earthquakes, Rain, Floods, Mudslides
  Tornados, Hurricanes, Tsunami
  Insect Damage, Materials Degradation
  Heat, Humidity, Moisture
Supply systems
  Communication Outages
  Power Distribution
  Bursting Pipes
  Gas Leaks

## Slide 3: Physical Security Threats
Man-made
  Sabotage / Fraud
  Mistakes, Disgruntled Workers
  Chemical Spills, Explosions
  Construction Failures / Building Collapse
Political Events
  Bombings, Terrorist Attacks, Civil Disturbances, Strikes, Espionage

## Slide 4: Designing a Physical Security Program
Deterrence
  Fences, warning signs, guards, dogs
Detection
  Intruder sensors, video surveillance
Delay tactics
  Locks, access controls
Situational Assessments
  Guard procedures, call trees
Response to intrusions/disruptions
  Response team/procedures, authorities

## Slide 5: Crime Prevention through Environmental Design (CPTED)
Physical Environment of a building can be managed to produce behavioral effects that reduce the incidence of crime
Territoriality Reinforcement: People protect territory that they feel they own and respect territory of others
Natural Surveillance: Intruders do not want to be seen
Natural Access Control: Properly located entrances, exits, and landscaping can control flow of people and help identify intruders

## Slide 6: Facility Planning
“Low visibility”
  Surrounding terrain
  Building markings and signs
  Neighborhood
Surrounding area and external entities
  Crime Rate
  Proximity to Police/Fire/Medical
  Possible hazards from surrounding areas

## Slide 7: Facility Planning
Accessibility
  Road access
  Traffic
  Proximity to airports, train stations, and highways
Natural Disasters
  Likelihood of floods, tornados, earthquakes, or hurricanes
  Hazardous terrain

## Slide 8: Data Center Cage Examples

## Slide 9: Data Center Wiring

## Slide 10: Personnel Access Controls
Facility
  Turnstiles
  Man traps
  Guards
Identification
  Photo IDs
  Magnetic ID cards
  Biometric devices
  CCTV
  IP Cameras

## Slide 11: Turnstiles

## Slide 12: Mantraps

## Slide 13: Personnel Access Controls
Proximity Readers
  User Activated – User swipes card, system lets person in
  System Sensing – Sensor can detect badges in proximity to sensor
  Two-factor (or multi-factor):
    Proximity reader /numeric keypad
    Hand geometry reader w/proximity or keypad or both
Card badge readers
  Transponders - Card and Reader have receiver, transmitter, and battery
  Passive Devices - Device is powered by reader

## Slide 14: Bio / 2-factor Access Controls

## Slide 15: Iris & Retina Scanning

## Slide 16: Biometric Accuracy
False Reject Rate (FRR)
  Type I error – rejects valid user
False Accept Rate (FAR)
  Type II error – allows invalid user
Crossover Error Rate (CER)
  Measurement between FRR and FAR
  Lower CER means a more accurate biometric system

## Slide 17: Auditing Physical Access
Processes & Logs (lots and lots of logs!)
  Date/time
  Location
  ID(s) used
  Access logs are a detective tool, not preventative!

## Slide 18: Cipher Locks (What’s wrong with the picture on the right?)

## Slide 19: Master Keying

## Slide 20: External Boundary Protection
Fencing & other physical barriers
Lighting
Intrusion detection
CCTV / IP Cameras
Patrol Force

## Slide 21: Fencing
Varying heights provide varying levels of protection
  3 -4 ft /1meter (deters casual trespasser)
  6 -7 ft/2meters (too high to climb easily)
  8 ft/2.4meters + 3 strands of barbed wire (deter determined intruder)
Grades of Fence
  Wire gauge (lower number = larger, heavier wire)
  Mesh size (2 in normal, 3/8 in is highest security)
  Can be costly
  May be unsightly, zoning considerations
Perimeter Intrusion Detection and Assessment System (PIDAS) can detect cutting or climbing

## Slide 22: Fence Examples

## Slide 23: Other Physical Barriers
Landscaping
  Shrubs can provide an alternative to fencing
  However tall trees can provide a shelter for intruders
Gates
  A movable barrier
  Entrapment – Condition where an object could get caught that may result in injury
Bollards / Vehicle (Physical) Barriers
  Heavy duty post to restrict vehicle traffic

## Slide 24: Physical Barriers / Bollards

## Slide 25: Other Vehicle Barriers

## Slide 26: ‘K' rating Crash Test Certification
A ‘K' rating is a Crash Test Certification issued by the Department of State (DoS) to a fence, gate, barrier or bollard indicating the perpendicular impact penetration of a vehicle of a specific weight at a specific speed. In other words, it measures the particular stopping power of a barrier in relation to the speed and weight of an incoming vehicle. The K-rating weight of the vehicle is standard at 15,000 lbs. These DoS standard barriers only allow the truck to penetrate no more than 36 inches past the bed.
K4 rating is for a vehicle traveling 30mph
K8 rating is for a vehicle traveling 40mph
K12 rating is for a vehicle traveling 50mph

## Slide 27: Physical Intrusion Detection
Intrusion detection/monitoring
Optical/light beams
Vibration sensors
Closed circuit TV
Motion detection
  Infrared
  Microwave

## Slide 28: Physical Intrusion Detection
Considerations:
  Expensive to install and monitor
  Requires human response
  Practical if fence not possible
  Subject to nuisance alarms (false positives)
  Can be penetrated

## Slide 29: Video Surveillance

## Slide 30: Patrol Forces
Guards
  Can provide flexible security & safety response
  Good deterrence
  May be effective for protecting group of buildings
  Costly
Guard Dogs

## Slide 31: Types of Alarms
Deterrent: Triggers deterrents such as locks, close doors, etc. – meant to contain or make further intrusion more difficult
Repellant: Sound an audio device, turn on / flash lights, etc. – used to discourage intruders or attackers from continuing or force off premises
Notification: Often silent, notifying others of the event, triggering recording (video, physical location, etc.) – used to bring authorities to the perpetrator in the hopes of catching them
Local System: Broadcast an alarm up to 120db that can be heard up to 400ft away – used to notify security or guards who can respond (similar to repellant)
Central Station: Usually silent locally, but alerting off-site agents who can respond – examples include Brinks, ADT, etc.
Auxiliary Station: Automatic notification added to local or central station – used to alert emergency services such as police, fire, medical, etc. (could result in fees for false alarms)
Combined: Two or more of the alarms can be incorporated in a single solution

## Slide 32: Power Terminology
Fault: A momentary loss of power
Blackout: A complete loss of power
Sag: Momentary low voltage
Brownout: Prolonged low voltage
Spike: Momentary high voltage
Surge: Prolonged high voltage
Inrush: An initial surge of power usually associated with connecting to a power source, whether primary or alternative / secondary
Noise: A steady interfering power disturbance or fluctuation
Transient: A short duration of line noise disturbance
Clean: Non-fluctuating pure power
Floating Ground: The wire in an electrical circuit that is grounded

## Slide 33: Uninterrupted Power (UPS)

## Slide 34: Static voltage damage levels
40: Destruction of sensitive circuits
1,000: Scrambling of monitor displays
1,500: Destruction of data stored on hard drives
2,000: Abrupt system shutdown
4,000: Printer jam or component damage
17,000: Permanent circuit damage

## Slide 35: Power sub-stations

## Slide 36: HVAC Environmental Conditioning
Freon
Glycol
Water
Positive pressure
What’s the right temperature?

## Slide 37: Computer Room Air Conditioners

## Slide 38: Fire
Combustion elements
  Fuel, Oxygen, Temperature
Suppression methods versus combustion elements
  Remove fuel / oxygen (CO2/soda acid)
  Reduce temperature (water)
  Interference with chemical reaction (Halon)

## Slide 39: Fire Suppression - Classes
A - Common combustibles
  Suppress with water/soda acid
B - Liquid
  Suppress with CO2/soda acid/Halon (Dry Chemical)
C -Electrical
  Suppress with CO2/Halon (Dry Chemical)
D –Combustible Materials (Magnesium, Sodium, Potassium)
  Dry Powder (NaCl, Graphite, Cu)
K – Cooking oils and fats (Grease)

## Slide 40: Fire Suppression Agents
Water
  Bad for electronics and buildings
CO2
  colorless, odorless, and potentially lethal in that it removes oxygen
  Bad for people
  Use built-in delay in manned areas
  Emergency shut off override
Halon
  Better for people
  Bad for environment (Ozone-depleting)
  Use built-in delay in manned areas
  Emergency shut off override

## Slide 41: Halon
Halogenated extinguishing agent
  Must be thoroughly mixed with air
  Montreal protocol (1987)
    stopped Halon production as of 01/01/94 due to agent releasing ozone-depleting substances
  Halon 1301 requires expensive pressurized flooding system
  Halon 1211 self-pressurizes (used in portable extinguishers)
FM-200 most effective alternative to Halon
Other Alternatives are NAFS-III, CEA-410, FE-13, Argon, Water, Inergon, or Argonite

## Slide 42: Types of systems
Wet pipe
  Always contain water
  Discharged by temperature control sensors
  Could cause damage in the event of a pipe break
Dry pipe
  Water is not in the pipe until a temperature is reached
  Typically a delay between detection and release of water
Pre-action
  Combination of Dry and wet pipe
  Water is release based on temperature, but sprinkler head doesn’t release water until a link is melted away
Deluge
  Dry pipe system with large volumes of water

## Slide 43: Fire Detection
Smoke Activated
  Photoelectric device detects changes in air particles
  Prone to false alarms
Heat activated
  Detect heat (fixed-temperature or rate of rise)
Flame activated
  Senses the pulsations of flames or infrared flame energy
  Expensive

## Slide 44: Fire prevention systems

## Slide 45: Fire prevention systems